## Slide 1: Plastic Auto Part Development
December 24, 2018
Anbo CAO, Feng CUI, Chendi JIANG
Notes: 此页可以删除

## Slide 2: Contents
1
Introduction
2
3
4
Topo-optimization
Reconstruction of the model
Result & Conclusion

## Slide 3: Contents
1
Introduction
2
3
4
Topo-optimization
Reconstruction of the model
Result & Conclusion

## Slide 4: Problem discription
A plastic bracket to mount “Electrical Park Brake” switch button

## Slide 5: Load definition
F=750N
33o

## Slide 6: Constraint definition
Rigid

## Slide 7: Main needs
Displacement: < 2mm
Bracket to deco box inner surface distance ≥ 5mm
Deco box wall thickness = 2.5mm

## Slide 8: Contents
1
Introduction
2
3
4
Topo-optimization
Reconstruction of the model
Result & Conclusion

## Slide 9: Original model
Console model
Original model

## Slide 10: Topo-optimized model

## Slide 11: Contents
1
Introduction
2
3
4
Topo-optimization
Reconstruction of the model
Result & Conclusion

## Slide 12: Design based on the optimized result
Shape the model to fit the console
Hollow out
Reinforcement by bars
Repeat the steps before to meet the needs

## Slide 13: View of the model in 4 directions

## Slide 14: Selection of material
The material we select | Tensile modulus (Gpa) | Density (g/cc) | Poisson ratio
PP | 12.8 | 1.44 | 0.4
Name | Tensile Modulus(Gpa) | Density(g/cc) | Source
Eurostar Starpylen MX06050 PP, 30% Glass Filled, Injection Molded | 5.7 | 1.12 | http://matweb.com/search/DataSheet.aspx?MatGUID=249d6a3ff64348e099ee2d9be629434e
PolyOne OnForce™ LFT PP-30 LGF/000 Natural PP Homopolymer with 30% Long Glass Fiber | 5.52 | 1.12 | http://matweb.com/search/DataSheet.aspx?MatGUID=588405dc61de489e953e23dfeebf4490
Celanese Celstran® +PP-GF30-04CN02/10 PP, 30% Glass Reinforced | 6.8 | 1.13 | http://matweb.com/search/DataSheet.aspx?MatGUID=d55780122e1946fe83536252e4ff63a5
Celanese COMPEL PP-GF30-04 PP, Glass Reinforced | 7.2 | 1.12 | http://matweb.com/search/DataSheet.aspx?MatGUID=d63691b9b8064590b23886de21c2beb3
RTP Company RTP 199 X 135006 A Polypropylene (PP) Glass Fiber - Flame Retardant - Non-PBB/PBDE | 6.89 | 1.51 | http://matweb.com/search/DataSheet.aspx?MatGUID=02cf7c08c06148bea347505aa29d0d81
RTP Company RTP 199 X 129987 B Polypropylene (PP) Glass Fiber - Chemically Coupled - Flame Retardant - Non PBB/PBDE | 7.58 | 1.54 | http://matweb.com/search/DataSheet.aspx?MatGUID=5e0a6f83e65a41dd8bf96504c6775f8d
RTP Company RTP 103 CC FR UV Polypropylene (PP), Glass Fiber Reinforced - Flame Retardant - UV Stabilized | 6.21 | 1.43 | http://matweb.com/search/DataSheet.aspx?MatGUID=21ff3d34204c4c36a1baed6ad2e6f46c
Plastcom SLOVALEN PH 69 GF 40 TS PP reinforced with 40% glass fibre, with modification of mechanical properties and thermal stabilization | 9.5 | 1.15 | http://matweb.com/search/DataSheet.aspx?MatGUID=ad4e5b0fb04b4d63b5cf12816fe48b6d
Plastcom SLOVALEN PH 49 GF 60 PP reinforced with 60% glass fibre | 12.8 | 1.44 | http://matweb.com/search/DataSheet.aspx?MatGUID=4407502b1ac0444e973cf836bbc6aeeb
RTP Company ESD 187 HF Polypropylene (PP) Carbon Fiber - High Flow - Electrically Conductive | 21.4 | 1.15 | http://matweb.com/search/DataSheet.aspx?MatGUID=c818439aedc241138d9ce5f0f086e947
RTP Company ESD 182 Polypropylene (PP), Carbon Fiber - Electrically Conductive | 8.27 | 0.97 | http://matweb.com/search/DataSheet.aspx?MatGUID=bac007a4be2e416da91f69e97cc18df3
RTP Company RTP 183 HI Polypropylene (PP), Carbon Fiber | 8.27 | 0.99 | http://matweb.com/search/DataSheet.aspx?MatGUID=30fa952597844370a894d50a1edd6a73
RTP Company ESD C 180 Polypropylene (PP), Carbon Fiber - ESD Protection - Electrically Conductive | 5.52 | 0.96 | http://matweb.com/search/DataSheet.aspx?MatGUID=85d2ad56a66345369fddcdba8e031bc4
RTP Company RTP 183 TFE 15 Polypropylene (PP), Carbon Fiber - PTFE Lubricated | 11.4 | 1.1 | http://matweb.com/search/DataSheet.aspx?MatGUID=96dde220e262486caebe3c1044d93718

## Slide 15: Verification of the design
Max displacement ≈ 1.8mm

## Slide 16: Verification of the design
Max stress ≈ 38.34MPa

## Slide 17: Contents
1
Introduction
2
3
4
Topo-optimization
Reconstruction of the model
Result & Conclusion

## Slide 18: Result
 | Mass (kg) | Volume () | Max displacement ()
Our design |  |  | 
 | Mass (kg) |  | 
Our design |  |  | 

## Slide 19: Price of the material
Still waiting for their response …

## Slide 20: Conclusion
The reinforcement with bars is efficient in increasing the stiffness of the model.
Triangle structure is quite stable.
The specific stiffness of the material is an important factor. A more appropriate material may be chosen to replace the present one.

## Slide 21
Thank you !